## Slide 1
Selected topics in solid state physics
Preparatory material for the 4mh laboratory
Rososhek Alexander

## Slide 2
SOLID MATERIALS
CRYSTALLINE
POLYCRYSTALLINE
AMORPHOUS
(Non-crystalline)
Single Crystal
Classification of solids

## Slide 3
Crystalline Solid is the solid form of a substance in which the atoms or molecules are arranged in a definite, repeating pattern in three dimension.
Crystalline solid

## Slide 4
Single Crystal
Single Pyrite
Crystal
Amorphous
Solid
Single crystal has an atomic structure that repeats periodically across its whole volume. Even at infinite length scales, each atom is related to every other equivalent atom in the structure by translational symmetry
Crystalline solid

## Slide 5
Every cubic cm contains about 1022 atoms; therefore, in ordered crystal every single-atom energy level is divided into 1022 different very dense levels. Hence, one might think of these levels as energy bands. In between every energy band there is an energy gap which contains forbidden energy levels.
X 1022
E
0
E1
E2
EV
Eex1
Eex2
Single atom
E
0
E1
E2
EV
Eex1
Eex2
crystal
Valence band, conduction band, and energy gap are important for the electrical conduction.
Conductance band
Energy gap
Eg (gap)
Conduction band
Valence band
Energy levels in a crystalline solid

## Slide 6
At 0K the valence band is full and conduction band empty - like Insulator.
When enough energy is supplied to the e- sitting at the top of the valence band, e- can make a transition to the bottom of the conduction band.
When electron makes such a transition it leaves behind a missing electron state.
This missing electron state is called as a hole.
Hole behaves as a positive charge carrier.
Magnitude of its charge is the same as that of the electron, but with an opposite sign.
Forbidden
energy gap [Eg]
Full
valance
band
Empty
conduction
band
+
e-
+
e-
+
e-
+
e-
energy
Semiconductors: electrons and holes

## Slide 7
Thermal energy
Electrical field
Electromagnetic radiation
Eg
Partially filled
CB
Partially filled
VB
Energy band diagram of a
s/c at a finite temperature.
Semiconductors: how to excite an electron?

## Slide 8
Thermal energy = k x T = 1.38 x 10-23 J/K x 300 K =25 meV
Excitation rate = constant x exp(-Eg / kT)
Although the thermal energy at room temperature, , is very small, i.e. 25 meV, a few electrons can be promoted to the CB.
Electrons can be promoted to the CB by means of thermal energy.
This is due to the exponential increase of excitation rate with increasing temperature.
Excitation rate is a strong function of the temperature.
1 - Thermal energy

## Slide 9
For low fields, this mechanism doesn’t promote electrons to the CB in common s/c’s such as Si and GaAs.
An electric field of 1018 V/m can provide an energy of the order of 1 eV. This field is enormous.
The use of the electric field as an excitation mechanism is not useful way to promote electrons in s/c’s.
2 - Electric field

## Slide 10
h = 6.62 x 10-34 J/s
c = 3 x 108 m/s
1 eV=1.6x10-19 J
To promote electrons from VB to CB Silicon , the wavelength
of the photons must 1.1 μm or less
Near
infrared
3 - Electromagnetic radiation

## Slide 11
The converse transition can also happen.
An electron in CB recombines with a hole in VB and generate a photon.
The energy of the photon will be in the order of Eg.
If this happens in a direct band-gap s/c, it forms the basis of LED’s and LASERS.
+
e-
Valence Band
Conduction Band
photon
3 - Electromagnetic radiation

## Slide 12
The conductivity of a pure (intrinsic) s/c is low due to the low number of free carriers.
For an intrinsic semiconductor
n = p = ni
n = concentration of electrons per unit volume
p = concentration of holes per unit volume
ni = the intrinsic carrier concentration of the semiconductor under consideration.
The number of carriers are generated by thermally or electromagnetic radiation for a pure s/c.
Intrinsic semiconductor

## Slide 13
The intrinsic carrier concentration ni depends on;
the semiconductor material
the temperature.
For silicon at 300 K, ni has a value of 1.4 x 1010 cm-3.
Clearly , equation (n = p = ni) can be written as
n.p = ni2
Intrinsic semiconductor

## Slide 14: What is doping and dopant impurities ?
To increase the conductivity, one can dope pure s/c with atoms from column III (starts with B) or V (starts with N) of the periodic table. This process is called doping and the added atoms are called dopant impurities.
n (negative) - type
p (positive) - type
Addition of different atoms modify the conductivity of the intrinsic semiconductor.
Donors and acceptors (extrinsic semiconductors)

## Slide 15
Boron atoms have three valence electrons, there is a deficiency of electron or missing electron to complete the outer shell.
Each added or doped boron atom introduces a single hole to the crystal.
There are two ways of producing a hole
1) Promote e-’s from VB to CB;
2) Add column III impurities to the s/c.
p-type doped semiconductor

## Slide 16
Ec = CB edge energy level
Ev = VB edge energy level
EA= Acceptor energy level
Eg
CB
VB
acceptor
(Column lll) atoms
Electron
Hole
p-type energy diagram

## Slide 17
The impurity atoms from column III occupy at an energy level within Eg . These levels can be
Shallow levels which are close to the band edge,
Deep levels which lie almost at the middle of a band gap.
If the EA level is shallow i.e. close to the VB edge, each added boron atom accepts an e- from VB and have a full configuration of e-’s at the outer shell.
These atoms are called as acceptor atoms since they accept an e- from VB to complete its bonding. So each acceptor atom gives rise a hole in VB.
The current is mostly due to holes since the number of holes are made greater than e-’s.
p-type doped semiconductor

## Slide 18
The number density, i.e., the number of electrons available for conduction in CB is
The number density, i.e., the number of holes available for conduction in VB is
Carrier concentration equations

## Slide 19
Charge concentration: intrinsic s/c
Example: intrinsic semiconductors at :
ni (Si) ≈ 1.2 x 1010 cm-3
ni (Ge) ≈ 2.4 x 1013 cm-3
ni (GaAs) ≈ 2.2 x 106 cm-3
As you may see these concentrations are significantly lower than the atom number density in a crystal ()
- effective electron mass
- effective hole mass
- energy gap between the VB and CB
per cm3

## Slide 20
s/c conductivity vs temperature